## Slide 1: PHYTON DRIVING LICENSE Exam project
Prof. Raos, Guido
Prof. Miglio, Edie
Prof. Bruschi, Francesco
Piccagli, Federico [10801916]
Leonardis, Giacomo [10575811]
Students ID:
Supervisors of the course:
Academic year: 2022 - 2023

## Slide 2: Introduction
Lead-cooled fast reactor (LFR) technology
IVth generation nuclear reactors
Next generation nuclear reactors
Materials challenges
GEN-IV FBRs
GEN-IV FBRs
Materials challenges
Materials challenges
Troubleshooting solutions
Materials solutions
Materials solutions
Fast Breeder Reactor (FBR) concepts
Materials requirements
[1] M. Vanazzi, PhD Thesis, Politecnico di Milano, 2019. [2] https://en.wikipedia.org/wiki/Lead-cooled_fast_reactor.
[2]
Aim of the current PhD project

## Slide 3: Introduction
IVth generation nuclear reactors
Next generation nuclear reactors
Materials challenges
GEN-IV FBRs
GEN-IV FBRs
Materials challenges
Materials challenges
Troubleshooting solutions
Materials solutions
Materials solutions
Materials requirements
[1]
Integrity of reactor’s in-core steel parts
[1] M. Vanazzi, PhD Thesis, Politecnico di Milano, 2019.
Heavy Liquid Metal (HLM) dissolution
Aim of the current PhD project

## Slide 4: Introduction
IVth generation nuclear reactors
Next generation nuclear reactors
Materials challenges
GEN-IV FBRs
GEN-IV FBRs
Materials challenges
Materials challenges
Troubleshooting solutions
Materials solutions
Materials solutions
Materials requirements
[1] M. Vanazzi, PhD Thesis, Politecnico di Milano, 2019.
Ceramic protective barriers
PLD-grown a-Al2O3 coatings
[1]
Aim of the current PhD project

## Slide 5: Introduction
IVth generation nuclear reactors
Next generation nuclear reactors
Materials challenges
GEN-IV FBRs
GEN-IV FBRs
Materials challenges
Materials challenges
Troubleshooting solutions
Materials solutions
Materials solutions
Materials requirements
Aim of the current PhD project
[1] M. Vanazzi, PhD Thesis, Politecnico di Milano, 2019.
Preservation of the film’s integrity
Corrosion-damage exposure
Radiation-damage exposure
Mechanical deformation
Focus of the project hereby presented
[1]

## Slide 6: Introduction
IVth generation nuclear reactors
Next generation nuclear reactors
Materials challenges
GEN-IV FBRs
GEN-IV FBRs
Materials challenges
Materials challenges
Troubleshooting solutions
Materials solutions
Materials solutions
Materials requirements
x
y
z
74 mm
4 mm
15 mm
Aim of the current PhD project
Planar dog-bone geometry
Externally imposed strain/stress
Evaluate the coating’s response upon mechanical deformations
TENSILE TESTS experimental campaign

## Slide 7: Experimental
Experimental analysis
Generation of dog-bone substrates from a cold-rolled AISI316 metal sheet
Pre-deposition treatments (grinding, polishing, ultrasonic cleaning, ion gun cleaning)
Retrive the conditions (stress or strain) upon which the coating failed i.e., cracked or delaminated
4. Mechanical tests with diverse tensile loads
3. Pulsed Laser Deposition of a- coatings with different thickness
5. Ex-situ characterization and analysis
SEM image of a cracked coating

## Slide 8: How Phyton is useful for?
Raw data as resulting from each tensile test
Stress-strain characteristics
Incremental modulus of the composite
Linear elastic approximation
Study of the fracture mechanics of the coating
Study of the mechanics of the whole composite

## Slide 9: Phyton Project
General overview of the assignment
Sequence of the operations leading to the expected result:
Creation of a test script for a random case study
Adjustment of the previous script to all case studies
Generation of re-elaborated scripts
Focus on:
DATABASE ANALYSIS
MANIPULATION OF RAW DATA
PLOTS AND DIAGRAMS
Phyton libraries adopted for the purpose:
MatPlotLib
NumPy/SciPy
Graphics
Mathematics
Scikit-Learn/Statistics
Data analysis
Pandas
Data manipulation

## Slide 10: Phyton project
Test script
Definition of useful functions
[3] https://it.wikipedia.org/wiki/Coefficiente_di_determinazione
[3]
analytical definition:

## Slide 11: Phyton project
Test script
Definition of useful functions
Raw data import from an excel file
Creation of a DataFrame containing the data to be analyzed
Raw data
Processed data

## Slide 12: Phyton project
Test script
Definition of useful functions
Linear interpolation
Creation of a DataFrame containing the data to be analyzed
The entire strain and stress columns of the DataFrame are collected into an array-like parameter (X and Y, respectively)
The “interp1d” class generates the interpolation function
The “linspace” class creates the interpolation points by specifying evenly spaced numbers over a specified interval (the entire strain column of the DataFrame)
The interpolated value is obtained by computing the interpolation function all over the prescribed interpolation points
Raw data import from an excel file

## Slide 13: Phyton project
Test script
Definition of useful functions
Raw data import from an excel file
Linear interpolation
Linear regression
Creation of a DataFrame containing the data to be analyzed
The entire strain and stress columns of the DataFrame are collected into a reshaped matrix-like parameter (X1 and Y1 respectively)
The “LinearRegression” class fits the x- and y- data (X1 and Y1, respectively) generating a straight line passing through the origin (specified by the “fit_intercept” parameter)
The estimated y-value as resulting from the linear regression is obtained by way of the “predict” method, applied to all the x-values (X1, in this case)
The incremental modulus is the slope of the linear regression straight line passing through the origin (divided by 1000 to have the result in GPa)

## Slide 14: Phyton project
Test script
Definition of useful functions
Raw data import from an excel file
Linear interpolation
Linear regression
Graphical analysis of the results
Creation of a DataFrame containing the data to be analyzed
“pyplot” class is used to display the stress-strain curve and the linear elastic approximation

## Slide 15: Phyton project
Test script
Definition of useful functions
Raw data import from an excel file
Linear interpolation
Linear regression
Graphical analysis of the results
Determination of the numerical results
Creation of a DataFrame containing the data to be analyzed
The value of the linear regression has been computed analytically by calling the “r2regression” function and with a specific class belonging to the scikit-learn library
A function determines the goodness of the linear elastic approximation performed so far
The incremental (elastic) modulus is returned as an integer, whose magnitude is in GPa
An additional library (“colorama”) is used to display colored text

## Slide 16: Phyton project
Analysis_RTdegC(2,0)
Definition of useful functions
Raw data import from an excel file
Creation of a DataFrame containing the data to be analyzed
If multiple sheets are imported contemporarily, the Pandas library creates a general dictionary
Each sheet corresponds to a diverse tensile load (experimental condition)
Every DataFrame must be extracted from the dictionary singularly
Adjustment of the test script to analyse 2 µm–thick coatings tensile tested at 25°C

## Slide 17: Phyton project
Definition of useful functions
Raw data import from an excel file
Linear interpolation
Linear regression
Graphical analysis of the results
Creation of a DataFrame containing the data to be analyzed
“pyplot” class (subplot method) is used to display the stress-strain curve and the linear elastic approximation for every tensile load applied by the tensile machinery
Analysis_RTdegC(2,0)
Adjustment of the test script to analyse 2 µm–thick coatings tensile tested at 25°C

## Slide 18: Phyton project
Definition of useful functions
Raw data import from an excel file
Linear interpolation
Linear regression
Graphical analysis of the results
Determination of the numerical results
Creation of a DataFrame containing the data to be analyzed
Analysis_RTdegC(2,0)
Numerical results are saved into appropriate lists (arrays)
A DataFrame collecting the results is then generated by adding each list one next the other
Adjustment of the test script to analyse 2 µm–thick coatings tensile tested at 25°C

## Slide 19: Phyton project
Definition of useful functions
Raw data import from an excel file
Linear interpolation
Linear regression
Graphical analysis of the results
Determination of the numerical results
Creation of a DataFrame containing the data to be analyzed
Adjustment of the test script to analyse 2 µm–thick coatings tensile tested at 25°C
Analysis_RTdegC(2,0)

## Slide 20: Phyton project
Definition of useful functions
Raw data import from an excel file
Linear interpolation
Linear regression
Graphical analysis of the results
Determination of the numerical results
Creation of a DataFrame containing the data to be analyzed
Adjustment of the test script to analyse 3 µm–thick coatings tensile tested at 25°C
Analysis_RTdegC(3,0)
“pyplot” class is used to display the stress-strain curve and the linear elastic approximation

## Slide 21: Phyton project
Definition of useful functions
Raw data import from an excel file
Creation of a DataFrame containing the data to be analyzed
If multiple sheets are imported contemporarily, the Pandas library creates a general dictionary
Each sheet corresponds to a diverse tensile load (experimental condition)
Every DataFrame must be extracted from the dictionary singularly
Adjustment of the test script to analyse 250 nm–thick coatings tensile tested at 25°C
Analysis_RTdegC(0,25)

## Slide 22: Phyton project
Definition of useful functions
Raw data import from an excel file
Linear interpolation
Linear regression
Graphical analysis of the results
Creation of a DataFrame containing the data to be analyzed
“pyplot” class (subplot method) is used to display the stress-strain curve and the linear elastic approximation for every tensile load applied by the tensile machinery
Analysis_RTdegC(0,25)
Adjustment of the test script to analyse 250 nm–thick coatings tensile tested at 25°C

## Slide 23: Phyton project
Definition of useful functions
Raw data import from an excel file
Linear interpolation
Linear regression
Graphical analysis of the results
Determination of the numerical results
Creation of a DataFrame containing the data to be analyzed
Numerical results are saved into appropriate lists (arrays)
A DataFrame collecting the results is then generated by adding each list one next the other
Analysis_RTdegC(0,25)
Adjustment of the test script to analyse 250 nm–thick coatings tensile tested at 25°C

## Slide 24: Phyton project
Definition of useful functions
Raw data import from an excel file
Linear interpolation
Linear regression
Graphical analysis of the results
Determination of the numerical results
Creation of a DataFrame containing the data to be analyzed
Analysis_RTdegC(0,25)
Adjustment of the test script to analyse 250 nm–thick coatings tensile tested at 25°C
!!!
The linear regression is not always possible and may run into errors in fitting the linear elastic regime

## Slide 25: Phyton project
Analysis_RTdegC(0,5)
Definition of useful functions
Raw data import from an excel file
Creation of a DataFrame containing the data to be analyzed
If multiple sheets are imported contemporarily, the Pandas library creates a general dictionary
Each sheet corresponds to a diverse tensile load (experimental condition)
Every DataFrame must be extracted from the dictionary singularly
Adjustment of the test script to analyse 500 nm–thick coatings tensile tested at 25°C

## Slide 26: Phyton project
Definition of useful functions
Raw data import from an excel file
Linear interpolation
Linear regression
Graphical analysis of the results
Creation of a DataFrame containing the data to be analyzed
“pyplot” class (subplot method) is used to display the stress-strain curve and the linear elastic approximation for every tensile load applied by the tensile machinery
Analysis_RTdegC(0,5)
Adjustment of the test script to analyse 500 nm–thick coatings tensile tested at 25°C

## Slide 27: Phyton project
Definition of useful functions
Raw data import from an excel file
Linear interpolation
Linear regression
Graphical analysis of the results
Determination of the numerical results
Creation of a DataFrame containing the data to be analyzed
Numerical results are saved into appropriate lists (arrays)
A DataFrame collecting the results is then generated by adding each list one next the other
Analysis_RTdegC(0,5)
Adjustment of the test script to analyse 500 nm–thick coatings tensile tested at 25°C

## Slide 28: Phyton project
Definition of useful functions
Raw data import from an excel file
Linear interpolation
Linear regression
Graphical analysis of the results
Determination of the numerical results
Creation of a DataFrame containing the data to be analyzed
Adjustment of the test script to analyse 500 nm–thick coatings tensile tested at 25°C
Analysis_RTdegC(0,5)
!!!

## Slide 29: Conclusions of the project
Results obtained with Phyton are in line with the MS Excel™ ones computed in a previous analysis
Phyton is an efficient and ready-to-use programming language
The broad range of libraries permits to cover every aspect of data processing and graphical analysis
Phyton permits to manage huge quantity of data with negligible computational times
A large community and a thorough online documentation can easily support programmers

## Slide 30: THANK YOU FOR YOUR KIND ATTENTION